Lake Township Ordinance No. ____

AN ORDINANCE AMENDING ORDINANCE NO. 	 OF

LAKE TOWNSHIP KNOWN AS THE SUBDIVISION

AND LAND DEVELOPMENT ORDINANCE OF LAKE TOWNSHIP

TO PROVIDE FOR THE REGULATION OF LARGE SCALE

SOLAR ELECTRIC ENERGY FACILITIES

#### Section 1. Title:

#### This Chapter shall be known as the Large-Scale Solar Electric Facility Ordinance for Lake Township.

##### Section 2.  Purpose:

The purpose of the Ordinance is to provide for the construction, installation, operation and decommissioning of Large-Scale Solar Electric Facilities in Lake Township, subject to reasonable conditions that will protect the public health, safety and welfare.

Section 3.  Definitions:

A.  “Applicant” is the Landowner or Developer, as those terms are defined in the Municipalities Planning Code and including their heirs, successors and assigns, who has filed an application for development of a Solar Electric Energy Facility under this Ordinance.

B.  “Facility Owner” means the person or entity having an equity interest in the Solar Electric Energy Facility, including their heirs, successors and assigns.

- “Operator” means the entity responsible for the day-to-day operation and maintenance of the Solar Electric Energy Facility.

- “Solar Electric System” means the components and subsystems that, in combination, convert solar energy into electric energy suitable for use. The term includes but is not limited to photovoltaic and concentrated solar power systems.

- “Solar Electric Energy Facility” means a Large-Scale Solar Electric Generating Facility, whose main purpose is to generate and supply electricity and consists of one or more Solar Electric Systems and other accessory structures and buildings, including substations, electrical infrastructure, transmission lines and other appurtenant structures and facilities.  These facilities shall not include Solar Electric Energy Systems meant for residential or commercial use.

- “Solar Farm”.  The location of the solar electric energy facility is situated.  The solar farm shall be located on a parcel or combined parcels of land with a minimum acreage of twenty (20) acres.

Section 4.  Applicability:

A.	This Ordinance applies to any Solar Electric Energy Facility proposed to be constructed after the effective date of the Ordinance.  Any pending application for a Solar Electric Energy Facility shall be subject to the requirements and conditions of this Ordinance under the Pending Ordinance Doctrine.

B.	A Solar Electric Energy Facility constructed prior to the effective date of this Ordinance shall not be required to meet the requirements of this Ordinance; provided that any physical modification or alteration to an existing Solar Electric Energy Facility that materially alters the size, type or components of the Solar Electric System shall require a permit under this Ordinance. Routine operation and maintenance or like-kind replacements do not require a permit.

Section 5.  Land Development Requirements:

A.  No land development plan providing for the construction or installation of a Solar Electric Energy Facility or addition of a Solar Electric System to an existing Solar Electric Energy Facility shall be approved unless such plan has complied with the requirements of this Chapter.

B.  The application or amended application shall be accompanied with a fee in the amount of One Thousand ($1,000) Dollars, also as escrow fee of $3,000.00 will be required at submission for Engineering and legal review fees.

C.  Any physical modification to an existing and permitted Solar Electric Energy Facility that materially alters the size, type and number of Solar Electric Systems or other equipment shall require a permit modification under this Ordinance.  Like-kind replacements shall not require a permit modification.

D.  No permit shall be issued for a Solar Electric Energy Facility unless the minimum lot size for a solar farm is depicted and thereafter verified on the permit application.

Section 6.  Additional Land Development Plan Requirements:

A.  Applications filed pursuant to this Ordinance shall comply with the Subdivision and Land Development Ordinance of Lake Township and shall contain the following:

1.  A narrative describing the proposed Solar Electric Energy Facility, including an overview of the project; the project location; the approximate generating capacity of the Solar Electric Energy Facility, the approximate number, representative types and height or range of heights of the panels or other Solar Electric System equipment to be constructed, including their generating capacity, dimensions and respective manufacturers, and a description of all ancillary facilities.

2.  An affidavit or similar evidence of agreement between the Landowner of the
real property on which the Solar Electric Energy Facility is to be located and the Facility Owner, demonstrating that the Facility Owner has permission of the Landowner to apply for necessary permits or approvals for construction and operation of the Solar Electric Facility ("Participating Landowner Agreement"). As a conditional requirement, the Facility Owner must provide a copy of an interconnection agreement with PJM and/or PPL and/or such other utility entity.

3.  Identification of the properties or portions thereof on which the proposed Solar Electric Energy Facility will be located, and the properties adjacent to where the Solar Electric Energy Facility will be located.  Identification shall include the name of the current property owner of the property proposed for the contemplated facility as well as all other adjoining owners by name and tax parcel numbers.  Identification shall also include any properties situated on any adjoining state or township roadway, for which the adjoining property owners share a common boundary line with the property upon which the facility is proposed.

4.  A site plan showing the planned location of each Solar Electric Facility
property lines, setback lines, access roads and turnout locations, substation(s), electrical cabling from the Solar Electric System to the substation(s), ancillary equipment, buildings and structures, including associated distribution and/or transmission lines, and layout of all structures within the geographical boundaries of any applicable setback.

5.  The projected cost of decommissioning must be set forth with supporting estimates by a qualified expert or company.

6. Such other relevant studies, reports, certifications and approvals as may be provided by the Applicant or required by the Lake Township Board of Supervisors recommended by the Township Engineers to ensure compliance with this Ordinance.

B.  Within thirty (30) business days after receipt of a land development application, Lake Township will determine whether the application is complete and advise the applicant accordingly.

Section 7.  Design and Construction:

- Design Safety Certification:  The design of the Solar Electric Energy System shall conform to applicable industry standards, including those of the American National Standards Institute. The Applicant shall submit certificates of design compliance obtained by the equipment manufacturers from Underwriters Laboratories (UL), IEEE, Solar Rating and Certification Corporation (SRCC), ETL, Florida Solar Energy Center (FSEC) or other similar certifying organizations.

B.  Uniform Construction Code:  The Solar Electric Energy Facility and the Solar Electric System shall be constructed to and comply with the Pennsylvania Uniform Construction Code, Act 45 of 1999, as amended, and any regulations adopted by the Pennsylvania Department of Labor and Industry as they relate to the UCC, except where an applicable industry standard has been approved by the Department of Labor and Industry under its regulatory authority.

C.	Visual Appearance: Power Lines

- Solar Electric Energy Facilities shall not be artificially lighted, except to the extent required by safety or by any applicable federal, state or local authority.

- Solar Electric Energy Facilities shall not display advertising, except for reasonable identification of the panel, inverter or other equipment manufacturer, and the Facility Owner.

3.  On-site transmission and power lines shall, to the maximum extent practicable, be placed underground.

D.	Fencing and Warnings:

- A Solar Electric Energy Facility shall be enclosed by a fence with a minimum height of seven (7’) feet, barrier or other appropriate means to prevent or restrict unauthorized persons or vehicles from entering the property.  Welding wire fencing is preferred over chain link fencing.

- Clearly visible warning signs shall be placed on the fence, barrier or Solar Electric Energy Facility perimeter to inform individuals of potential voltage hazards.

3.  Additional Visual Appearance Requirements:

Where in the judgment of the Board of Supervisors, and concerns of neighboring property owners, natural vegetation may be required along the perimeter fencing.  In the event that natural vegetation is dead, it shall be replaced within ninety (90) days of said event, or in the event of winter, by the first of May.

E.  Entrance Road

The Applicant shall depict the location of any entrance to the proposed solar farm upon an accompanying map to the application.  The entry road shall be a minimum of twenty-five (25’) feet wide from the intersection with a public highway to the inverter/transformer.  The entry road shall be maintained by the facility owner to provide access for any emergency vehicles. The Township reserves the right to name any entrance road for emergency and 911 purposes.  The Applicant shall be responsible for any costs associated with the naming of the entrance road for emergency and 911 purposes.

Section 8.  Setbacks:

A.	Property lines:  All Solar Electric Energy Systems shall be located one hundred (100) feet from all property lines where the System is located.  These distances shall be measured from the closest edge of the Solar Electric Energy System to the property line.

B.	A Solar Electric Energy Facility shall be sited in such a way that it presents no threat to traffic or to public health and safety.

Section 9.   Change of Ownership

Any change of ownership of the Facility Owner whether by deed and/or transfer of shares of a corporate entity and/or of a limited liability company, whether in whole or fractional part, shall require notification to the Township within thirty (30) days of said transfer occurrence.

# Section 10.  Decommissioning:

A.	The Facility Owner and Operator shall, at their expense, complete decommissioning
of the Solar Electric Energy Facility or individual Solar Electric Systems within twelve (12) months after the end of the useful life of such Facility or System. A Solar Electric Energy Facility or System will be presumed to be at the end of its useful life if no electricity is generated for a continuous period of twelve (12) months.

B.	Decommissioning shall include removal of all Solar Electric Energy Systems, buildings, cabling, electrical components, roads, foundations and any other associated facilities.

C.  Disturbed earth shall be graded and re-seeded, unless the landowner requests in
writing that the access roads or other land surface areas not be restored.

D.  The estimated cost of decommissioning shall be secured by a Bond or such other security to ensure the completed decommissioning of the Solar Electric Energy components.  The estimate will be reevaluated every 3 years to maintain the correct Bond or security amount is accurate for decommissioning costs.

Section 11.  Remedies:

A.	It shall be unlawful for any person, firm or corporation to violate or fail to comply
with or take any action that is contrary to the terms of this Ordinance or a permit issued under
this ordinance or cause another to violate or fail to comply, or take any action which is contrary
to the terms of this Ordinance or a permit issued under this Ordinance.

B.	If, after thirty (30) days from the date of the notice of violation, Lake Township 
determines, in its discretion, that the parties have not resolved the alleged violation, Lake Township may institute civil enforcement proceedings or any other remedy at law or

inequity to ensure compliance as provided in the Lake Township Subdivision and Land Development Ordinance.

Section 12.  Effective Date:

This ordinance shall take effect within five (5) days of enactment.

Attest:				     			LAKE TOWNSHIP BOARD

OF SUPERVISORS:

_______________________________

Secretary				 	    _____________________________________

Supervisor

_____________________________________

Supervisor

____________________________________	 								Supervisor